## Slide 1
VALENCIA COLLEGE
Department of Electrical & Computer Engineering Technology
EET 4910 — Senior Design Proposal
Safe Dip
A Safety-Oriented Hot-Dip Pick-and-Place System
Submitted by
Josué Bouchard | Adriano Mena
Supervised by Mayra Socarras
July 31, 2026
1
Notes: Adriano/Josue
Welcome to the presentation of Safe Dip

## Slide 2
Meet the team
Originally from Argentina
B.S. E.C.E.T., Computer concentration
Laboratory aide and embedded-systems enthusiast
Interested in robotics and aerospace
Originally from Cuba
B.S. E.C.E.T., Electrical concentration
Enjoys electrical projects and hardware design
Interested in robotics and aerospace
2
Notes: Adriano/Josue

## Slide 3
Presentation Roadmap
01
Problem & Motivation
Hazards of manual hot-dip coating
02
System Concept & Requirements
Safe Dip architecture and testable requirements
03
Mechanical Design
Frame, axes, motors, and end effector
04
Electrical & Power
Power distribution, sensing, and safety systems
05
Software & Control
Cooperative architecture and cycle sequencing
06
Preliminary Work & Conclusion
Modbus TCP and stepper signal validation
3
Notes: Adriano

## Slide 4
Hot Dipping
4
Notes: Adriano

## Slide 5
The Problem: Manual Hot-Dip Coating
Thermal Exposure
Workers handle parts near molten wax or resin at elevated temperatures
Burn & Splash Risk
Hot, viscous materials cause serious injuries from even small splashes
Repetitive Strain
Sustained repetitive motion injuries from manual dipping cycles
Weight Limitations
Tongs and clippers add physical strain beyond a few kilograms
Manual dipping remains one of the more
accident-prone tasks on the shop floor
5
Notes: Adriano

## Slide 6
Safe Dip: System Concept
A two-axis Cartesian gantry that automates the pick, dip, and place cycle
Three Stations
Input, dipping bath, and output positions
Safety-First
Hardwired Category 0 E-stop independent of microcontroller
INPUT
STATION
→
DIPPING
BATH
→
OUTPUT
STATION
Gantry beam (horizontal axis)
An interface will be exposed for the conveyor belts, but they are not considered part of the system
6
Remove the Operator
Eliminates direct exposure to heat and burns
Allows for Chemical Flexibility
Same platform works with wax, resin, or any treatment chemicals
Notes: Adriano

## Slide 7
Similar Products: Market Gap
7
Product
Price
Pick & Place
Variable Dip
Chem. Flex.
Safe Dip (Ours)
~$500-$600
YES
YES
YES
EFFCO DS-250
$15k-$25k
NO
NO
YES
MS800 Tiltable
$40k-$80k
NO
NO
YES
Monorail Screw
$3k-$4k
NO
NO
Partial
Thread Coater
$20k-$30k
NO
NO
NO
Emmeti WAX-ON
$50k-$150k+
YES
YES
Partial
South Shore Dip Cell
Custom
YES
YES
YES
Safe Dip is the only system under $1,000 that combines pick-and-place, variable dip depth, and chemical flexibility
Notes: Josue

## Slide 8
Operational Limitations
General Limitations
• Two-axis motion only
  Horizontal (transfer) + vertical (pick/dip/place). No rotation or lateral movement.
• Cylindrical workpieces
  Designed for cylindrical parts within specified size and payload limits.
• Ferromagnetic surface required
  Workpiece needs a clean, flat, ferromagnetic attachment area. This contact zone is not coated.
• Fixed input position
  No alignment, orientation correction, or vision-based localization.
Prototype-Specific Limitations
• Max payload: 1 lb
  Validated operating range. Heavier payloads are outside the prototype's tested capacity.
• Thermal design out of scope
  Heat affects frame, wiring, sensors, motors, and lubrication. Industrial thermal design is future work.
• Focus: control & safety
  Prototype seeks to demonstrates electrical, control, sensing, comms, and orientation to safety systems.
8
Notes: Josue

## Slide 9
System Requirements (SR-01 to SR-11)
9
SR-01
No motion unless workpiece detected at input
SR-02
Position end effector at pickup within ±1 cm
SR-03
Retain workpiece through full cycle without dropping
SR-04
Lower to immersion depth within ±1 cm
SR-05
Hold dwell time within ±1 s
SR-06
Complete one unattended pick-dip-place cycle
SR-07
E-stop removes power from both motor drivers
SR-08
System stays inhibited after E-stop until reset + restart
SR-09
Transmit operating state and faults via comms
SR-10
Complete 10 consecutive cycles without failure
SR-11
Full cycle with max weight of 1 lb workpiece payload
Each requirement has a defined pass/fail test condition
Notes: Josue

## Slide 10
System Block Diagram
10
Seven Functional Modules
Power Distribution
E-Stop & Protection
Processing (MCU)
Sensing
Movement
End Effector
Communications
Notes: Adriano

## Slide 11
Power Distribution Specifications
Mean Well LRS-350-48 AC-DC power supply
ALITOVE DC 12V 5A Power Supply
HiLetgo buck converter
11
Notes: Adriano

## Slide 12
E-Stop & Protection Specifications
E-stop mushroom button
12
Notes: Adriano

## Slide 13
Processing Specifications
STM32 Nucleo-F446RE microcontroller board
74HCT244 Octal Buffers and Line Drivers
13
Notes: Adriano

## Slide 14
Sensing Specifications
vl53l0x ToF sensor
14
Limit Switch
Notes: Adriano

## Slide 15
Movement Specifications
NEMA 23 23HS22-2804S stepper motor
DM542TE stepper controller
15
Notes: Adriano

## Slide 16
Communications Specifications
W5500 Ethernet module
16
Notes: Adriano

## Slide 17
End Effector Specifications
Baomain BM-P 80-38 electromagnet
17
MOSFET
1N4007 Flyback Diode
Notes: Adriano

## Slide 18
Detailed Block Diagram
18
Notes: Adriano
Power rails en colores
Seniales en negro
Modulos con linea punteada

## Slide 19
Mechanical Architecture
19
Built from standard commercial extrusion and linear-motion components — no custom machining required
Frame
4040 T-slot aluminum extrusion
Horizontal beam, vertical column, supporting legs
Horizontal Drive
Timing belt
Converts stepper rotation to fast linear travel
Vertical Drive
Leadscrew
Converts stepper rotation to precise linear travel
Preliminary Dimensions
Overall size
108 × 60 × 80 cm
Horizontal travel
≈100 cm
Vertical travel
≈30 cm
Bath envelope
30 × 30 × 30 cm
Clearance above bath
≈5 cm
Max workpiece
10 × 10 cm
Guides
Linear rails + carriages
Smooth movement
Notes: Adriano

## Slide 20
Power Distribution & Budget
20
Three Voltage Rails
48V
Stepper motors + drivers
Mean Well LRS-350-48 (7.3A, 350W)
12V
Electromagnet + low-voltage circuitry
ALITOVE DC 12V 5A (60W)
5V
Processing module + sensors
HiLetgo buck converter (XL4016, 12V→5V)
Power Budget Summary
Subsystem
Power
Movement (motors)
268.8 W
Movement (drivers)
~48 W
End Effector
26.88 W
Sensing + Comms + Processing
~2 W
Total Operational
~ 346 W
Available (adapters)
~ 410 W
Notes: Josue

## Slide 21
Monetary Budget
Generic Name | Component | Price per Unit | Price total
Single Output Switchable Power | Mean Well LRS-350-48 | $35.06 | $35.06
Microcontroler | STM32 NUCLEO-F446RE | $31.00 | $31.00
4‑channel digital buffer/line driver | SN74AHCT125N Quadruple Buffer | $0.80 | $0.80
Stepper Motor | 3HS22-2804S Nema 23 | $13.37 | $26.74
Stepper Controler | DM542TE Stepper Controller | $21.00 | $42.00
Ethernet Module | W5500 Ethernet LAN Network Module Support | $6.50 | $6.50
E-Stop | 1NC 1NO Red Mushroom Emergency Stop | $9.99 | $9.99
Transformer | ALITOVE Power Supply Adapter Converter Transformer | $14.00 | $14.00
Buck Converter | LM2596 DC a DC Buck | $1.60 | $1.60
Electro Magnet | Electromagnet Solenoid BM-P 80-38 | $44.98 | $44.98
Proximity Laser Sensor | VL53L0X ToF sensor | $2.98 | $2.98
Shaft Coupler | Shaft coupler (6.35x8mm) | $6.00 | $11.99
Limit Switch | HiLetgo Micro Interruptor de Límite KW12-3 | $0.60 | $0.60
Rail Guide | MGN12H 300mm Linear Rail Guide | $18.00 | $35.99
Lead Screw | Tr8x2 Lead Screw (300mm) | $11.99 | $11.99
Bearings | Pillow Block Bearing 4Pcs, 5/16" (8mm) | $2.12 | $8.49
Guide Rails | Linear Rail Slide SBR20-800mm | $22.45 | $44.90
Belt | 3D Printing GT2 Timing Belt | $16.88 | $16.88
Aluminum Beams | 4040 T-Slot Extruded Aluminum Profile 1000mm | $20.00 | $79.99
Relay | One Channel Relay Module Relay Switch | $3.70 | $7.39
Buzzer | Gikfun Terminals Passive Electronic Buzzer | $0.90 | $1.80
MOSFET Transistor | RLZ44N IRLZ44 MOSFET Transistors | $1.00 | $4.00
Terminal Block | Glarks Terminal Block Set | $0.13 | $0.26
Flyback Diode | BOJACK 1N4007 Rectifier Diode | $0.05 | $0.05
Wires | 22 AWG Stranded Wire Spool | $12.29 | $12.29
Cable Wrap Insulation | Eventronic Heat Shrink Tubing 2:1 | $6.99 | $6.99
Fuse Holder | FEBRYTOLD 0 Gauge Inline Fuse Holder | $4.25 | $4.25
Resistors kit | Upvivi Resistor Assortment Kit | $6.99 | $6.99
T-nuts | 4040 Series T Sliding Nuts Hammer Nut Block Square | $0.67 | $9.99
Bolt and Nuts Kit | Button Head Socket Cap Screws Bolts Nuts Kit M5 | $16.99 | $16.99
Motor Mounting | Nema 23 Stepper Motor Steel Mounting Bracket | $3.00 | $11.99
Nut Block | Lysee 3D Printer Parts & Accessories | $10.10 | $20.19
Converyor Belt | DC 12V Electric Desktop Conveyor Belt | $99.51 | $99.51
Total without conveyor: $525.37
Total with conveyor (before tax): $624.88
Other Products:
- Dip-Spin (EFFCO DS-250) est. $15k–$25k
- MS800 Tiltable Dip-Spin est. $40k–$80k
- Emmeti WAX-ON est. $50k $150k+
21
Notes: Josue

## Slide 22
Software Architecture: Cooperative & Nonblocking
22
Key Principles
Nonblocking Design
Each module performs bounded work and returns immediately.
No blocking while waiting for operations to finish
Cooperative Multitasking
Main loop steps: sequencer → movement → effector → timers → communications
Encapsulation
Sequencer does not directly manipulate timer registers, GPIO, or step counts. The different modules do.
Notes: Josue

## Slide 23
E-stop and Sequencer
23
Notes: Josue

## Slide 24
Instruction Start and Instruction
24
Notes: Josue

## Slide 25
Preliminary: Modbus TCP Communications
25
What Was Validated
Portable Modbus server library in C with no dynamic allocation
Supports coils, discrete inputs, input registers, and holding registers
W5500 manages Ethernet/TCP sockets; STM32 polls via SPI
Successfully tested: read-coils, write-single-coil, write-multiple-coils
Notes: Josue

## Slide 26
Preliminary: Stepper-Motor Signal Generation
TIM2 Output Compare Mode
Timer peripheral controls output transitions, not the main loop
Changing the half_period changes the Pulse Train Output frequency without software delays or blocking loops
26
Notes: Josue

## Slide 27
Gantt Chart
27
Notes: Josue

## Slide 28
Conclusion & Future Work
What Safe Dip Achieves
Removes operator from hazardous hot-dip environment
Two-axis Cartesian gantry with controlled pick-dip-place cycle
Category 0 E-stop with load-holding magnet design
Modbus TCP + serial communications for monitoring and control
Lower-cost, modular alternative to industrial robotic systems
Future Improvements
Thermal protection for heated bath operation
Transparent physical enclosure with interlocked access
Electro-permanent magnet for fail-safe load retention
Backup battery on electromagnet rail for total power loss
Questions & Discussion
Josué Bouchard | Adriano Mena | Supervised by Mayra Socarras
28
Notes: Josue

## Slide 29
References:
[1]“What is Hot Melt Wax Coating for Tools?,” Jul. 13, 2022, Dip Seal Plastics, Inc. Accessed: Jun. 25, 2026. [Online]. Available: https://www.dipseal.com/plastic-dipped-parts-tools and-corner/what-is-hot-melt-wax-coating-for-tools
[2] D. Dominessy, “End Mill Hot-Dip Wax Coating.” Accessed: Jun. 25, 2026. [Online]. Available: https://www.youtube.com/watch?v=gGHxNu6oPSY
[3] “What is the difference between Stop Category 0, Stop Category 1 and Stop Category 2?,” Feb. 28, 2014, Schneider Electric. Accessed: Jul. 05, 2026. [Online]. Available: https:// www.se.com/eg/en/faqs/FA225420/
[4] “Safety of machinery — Electrical equipment of machines — Part 1: General requirements,” International Electrotechnical Commission, IEC 60204-1:2016+A1:2021, Sep. 2021. Accessed: Jul. 20, 2026. [Online]. Available: https://webstore.iec.ch/en/ publication/71256
[5] “Thrust generation principle of a linear lead screw motor,” MOONS' Industries. Accessed: Jun. 25, 2026. [Online]. Available: https://www.moonsindustries.com/article/thrust generation-principle-linear-lead-screw-motor
[6] IQS Directory Editorial Team, “Lead Screws: What Is It?, How It Works, Types, and Advantages,” Jun. 16, 2026. Accessed: Jun. 26, 2026. [Online]. Available: https://www. iqsdirectory.com/articles/ball-screw/lead-screws.html
[7] RipInPease, “madbus-cli: A modbus tui using the madbus crate,” Mar. 18, 2026. Accessed: Jul. 04, 2026. [Online]. Available: https://lib.rs/crates/madbus-cli
[8] “EFFCO DS-250 Dip-Spin Coating Machine.” Accessed: Jul. 20, 2026. [Online]. Available: https://www.aramfix.com/product/effco-ds-250-dip-spin-coating-machine 250mm-basketxlxwxh-1500x1500x1890mm-steel-alloy-blue-1-pce
[9] “MS800 Automatic Tiltable Dip-Spin Coating Machine.” Accessed: Jul. 20, 2026. [On line]. Available: https://www.shishengst.com/shisheng-group-sale-ms800-automatic tiltable-dip-spin-coating-machine.html
[10] “TH-2004L3 Thread Coating Machine.” Accessed: Jul. 20, 2026. [Online]. Avail able: https://www.tianhaodispensing.com/products/coating-machine/thread-coating machin-TH-2004L3-D.html
[11] “Automatic Thread Coating Machine.” Accessed: Jul. 20, 2026. [Online]. Avail able: https://www.tianhaodispensing.com/products/coating-machine/thread-coating machine-automatic.html
[12] “Custom Automation and Specialty Equipment.” Accessed: Jul. 20, 2026. [Online]. Available: https://southshorecontrols.com/specialty-equipment/
[13] “UR5e Collaborative Industrial Robot.” Accessed: Jul. 20, 2026. [Online]. Available: https://www.universal-robots.com/manuals/EN/HTML/SW10_12/Content/ Landingpages/WebPolyX/LandingarmUR5e.htm
29
Notes: Adriano/Josue